## Slide 1
SMART INDIA HACKATHON 2026
PRAHARI
AI video-intelligence layer for existing CCTV infrastructure · SIH-suggested name: IBVAP
PROBLEM STATEMENT ID
26187
PROBLEM STATEMENT TITLE
AI-Based Intelligent Video Analytics Platform for Border Surveillance using Existing CCTV Infrastructure
THEME
Blockchain & Cybersecurity
PS CATEGORY
Software
ORGANISATION
Ministry of Home Affairs
DEPARTMENT
Sashastra Seema Bal (SSB), Police II Division
TEAM ID
[Team ID]
TEAM NAME (REGISTERED ON PORTAL)
[Team Name]

## Slide 2
THE PROBLEM
Border CCTV that nobody can fully trust
Real-world issue
Border-outpost cameras are installed over a decade, by different vendors, to different standards. Operators don't know what a camera can resolve, and metered VSAT/4G uplinks drop as a normal part of every week.
Why it matters
SSB secures both fenced sectors and treaty-open borders (Indo-Nepal, Indo-Bhutan) with heavy lawful daily traffic. A system that floods operators with false alerts gets muted by night three — the real crossing on night four gets muted too.
Our Solution
Prahari measures what each camera can actually see, runs detection, tracking and ANPR only where the imagery supports it, rations operator attention instead of drowning it, and keeps sensing — never just reporting — when the link goes down.
RISK → ENGINEERED RESPONSE
Unknown camera capability
→
Measured Capability Certificate — self-calibrated, IEC 62676-4 DORI bands
Alert fatigue from repeat false alarms
→
Alert governor rations attention + patrol-conformance suppression
Connectivity loss = blind spot
→
Offline-first edge — detection never depends on the link
Disputable evidence after the fact
→
Hash-chained, sealed, tamper-evident evidence trail
PROBLEM & SOLUTION
PRAHARI · SIH26187
2

## Slide 3
PS26187 REQUIREMENT MAPPING
Every asked-for capability, and how Prahari delivers it
REQUIREMENT (AS STATED IN PS26187)
STATUS
HOW PRAHARI DELIVERS IT
Human detection & tracking
BUILT
YOLOX-Tiny + ByteTrack; every confirmed track carries a global ID
Vehicle detection & classification
BUILT
Vehicle object classes feed both tracking and the ANPR gate
Face detection
BUILT
Detected only where the certificate supports it — recognition stays withheld, by policy
Automatic Number Plate Recognition
BUILT
fast-alpr (ONNX); reads only inside a camera's measured 250 px/m band
Virtual fence intrusion detection
BUILT
Tripwire & restricted-zone rules — the fenced-sector doctrine
Suspicious / behavioural activity
BUILT
Learnt pattern-of-life model, plus patrol-deviation escalation
Night-time movement detection
SUPPORTED
Thermal/IR is first-class today; a thermal-trained model is on the roadmap
Real-time alerts & event logging
BUILT
Alert governor + sealed, hash-chained ledger, live over WebSocket
Command & control integration
BUILT
REST + WebSocket API, sector-core aggregator; radar/PIDS fusion hook is defined, not yet built
PS COVERAGE
PRAHARI · SIH26187
3

## Slide 4
DIFFERENTIATORS
Eight things Prahari does differently
Measured, not declared
Camera capability is self-calibrated from pedestrians in-frame — no survey, no calibration target.
Two border doctrines
Tripwire rules for fenced sectors; pattern-of-life rules for treaty-open borders. Selectable per camera.
Alerting is rationed
Recording is always complete. Alerting is budgeted, so operators see the most significant events, not the first.
ANPR refuses to guess
Plates are read only inside the image band a camera's measured geometry can actually support.
Evidence is hash-chained
Every event commits to the one before it — a disconnected node's backlog becomes checkable, not just trusted.
Offline is the design point
Detection never depends on the link. Metadata is pushed; video is pulled when asked for.
Cameras form a corridor
A topology graph links tracks across cameras into one global identity — not five unrelated events.
Patrols are recognised
Matched against a declared route, window and direction — a patrol behaving oddly is escalated, not muted.
DIFFERENTIATORS
PRAHARI · SIH26187
4

## Slide 5
TECHNICAL APPROACH
Edge-first architecture — the link is optional
Existing CCTV
RTSP / ONVIF
PRAHARI-EDGE · at the Border Outpost
Profiling
→
Detection
→
Tracking
→
Rules
→
Scoring
Alert Governor
rations operator attention
Evidence + Hash Chain
sealed, tamper-evident
SQLite (WAL) + local evidence disk
metadata pushed,
video pulled
PRAHARI-CORE
sector aggregator
TECHNOLOGY STACK
Inference
ONNX Runtime — ~50 MB, one code path for CPU/CUDA, avoids YOLO's AGPL-3.0 licence
ANPR
fast-alpr (MIT) — detection + OCR both in ONNX, no torch dependency
Storage
SQLite, WAL, synchronous=FULL — survives power loss, no server to babysit
Message bus
In-process, NATS-shaped subjects — a broker is a process to fail, for no gain at edge scale
Frontend
Zero-build vanilla JS — a node needing npm can't be recovered from a USB stick
Map
Hand-drawn SVG — the console must render without internet
TECHNICAL APPROACH
PRAHARI · SIH26187
5

## Slide 6
FEASIBILITY & VIABILITY
Why this is buildable, credible and adoptable
Feasibility
Works with existing IP cameras / NVR feeds — no camera replacement
No Docker, no Node build step — Python 3.11+ only, native path
ONNX Runtime (~50 MB) instead of a ~2.5 GB deep-learning framework
Incremental rollout — a handful of BOPs first, expanded sector by sector
Functional on CPU alone; an RTX 4050-class 6 GB GPU covers the prototype
Viability
Detection, tracking and ANPR are solved problems — the contribution is the deployment architecture
Capability grading follows IEC 62676-4 DORI bands, not an in-house heuristic
Evidence design built with the DPDP Act 2023 and Bharatiya Sakshya Adhiniyam 2023 in view
Self-calibration verified to 0.2–3.2% error against the live, noisy pipeline
Business Potential
Sits inside CIBMS as the video-intelligence layer, alongside radar and PIDS — not a competing system
71–97% of raw rule events suppressed before they ever interrupt an operator
99.56–99.86% bandwidth reduction vs continuous streaming — viable on metered VSAT/4G
ONNX avoids Ultralytics YOLO's AGPL-3.0 licence — a real procurement consideration for government use
FEASIBILITY & VIABILITY
PRAHARI · SIH26187
6

## Slide 7
IMPACT & MEASURED RESULTS
Real numbers from the running pipeline, not projections
0.2–3.2%
Camera-height profiling error
self-calibrated, scored against the live pipeline
71–97%
Alert suppression
raw rule events reduced before reaching an operator
99.56–99.86%
Bandwidth reduction
event-only mode vs. continuous streaming
~2.5 KB
Per sealed event record
vs. a ~14 MiB evidence clip kept at the edge
Alert suppression by camera — evaluation harness
Chart: 
| CAM-011 Gate | CAM-014 Perimeter | CAM-022 Open border | CAM-031 Thermal | CAM-045 Legacy
Alert suppression % | 92 | 93 | 71 | 94 | 97
Why the bandwidth number holds up
Push metadata, pull video — an event record ships in a few hundred bytes; a multi-megabyte clip stays at the edge until requested.
Measured against this node's own encoded frames at its own settings during the run — not a brochure figure.
Under storage pressure, clips are evicted before records are — a weakened event is recoverable, a missing one is not.
IMPACT & RESULTS
PRAHARI · SIH26187
7

## Slide 8
STATED PLAINLY
What's proven today, and what isn't yet
A camera that can't resolve a plate doesn't get granted ANPR — it says why. This project holds itself to the same rule.
Measured and working today
Ground-plane self-calibration — 0.2–3.2% error, live pipeline
Alert governance — 71–97% of raw events suppressed
Offline queue, sync and hash-chain verification, tested end to end
Cross-camera handoff — 150 global entities, 2 linked, live on the demo node
Patrol-conformance suppression — all five reference scenarios verified
Evidence sealing with tamper-evident hash chaining
On the roadmap
Field validation on real Indian border footage — night, range, fog (the largest open item)
A proper cross-camera re-identification model — today's cue is an HSV colour signature
Duty-roster ingestion for patrol profiles, entered by hand today
GPU latency / VRAM characterisation for SAM 2 segmentation, on an idle GPU
Thermal-specific detection models — an RGB model on thermal is a compromise
Radar / PIDS sensor-fusion — the integration hook exists; fusion is not built
LIMITATIONS & ROADMAP
PRAHARI · SIH26187
8

## Slide 9
RESEARCH & STANDARDS
What Prahari is built against
IEC 62676-4
DORI bands govern every capability grant
ByteTrack
Two-stage association behind the tracker
MOT17
Detection & CLEAR-MOT/IDF1 benchmarking
DPDP Act, 2023
Data-minimisation posture by design
Bharatiya Sakshya
Adhiniyam, 2023
Evidence-chain design considers admissibility
CIBMS
Prahari positioned as the video layer within it
“Prahari is the video-intelligence layer of a multi-sensor border system. The video layer is implemented and measured. Integration with radar and PIDS is a defined extension point, not a delivered capability.”
TEAM
[Team Name] · Team ID: [Team ID]
PROBLEM STATEMENT
SIH26187 · Blockchain & Cybersecurity
RESEARCH & TEAM
PRAHARI · SIH26187
9